## Slide 1: Beta Altera Floorplan Results

## Slide 2: Altera Freedom level
Dealing with an Altera Board gives us a great degree of freedom in creating partially reconfigurable regions. Every block on the board could ideally be a region, this means that in a 220x175 blocks board we could generate 38500 regions.

## Slide 3: Freedom Price
This great freedom degree gives us a lot of possibilities when it comes to choosing a possible area for a region, but this makes our choice incredibly computationally heavy.

## Slide 4: Problem Example
Let’s think for a moment at a problem with N regions, each of them requiring just one block (suppose 1 LAB). Even excluding the reducible areas (areas bigger than what actually needed, such as a 2x2 area in this case) each region has 38500 possible positions, this means N*38500 possible areas! (192500 for just 5 regions)
This is clearly too much to handle in a reasonable time.

## Slide 5: Proposed Solution
The way we propose to tackle this problem is reducing this freedom by “discretizing” the board, this ,in general , prevent the solution from reaching the global optimum, but it allows the computation to end in a reasonable time.

## Slide 6: Discretization Example

## Slide 7: Discretization
In the previous example we discretized a 220x175 board into a 86x10 representation, this allows us to work with a reasonable number of possible areas.

## Slide 8: Future ideas
In very critical cases this discretization could affect the feasibility of the solution and not only its performance (e.g. : in the previous solution 11 regions that requires the exact amount of blocks of one row in the original fpga).
For this particular cases we thought that if a feasible solution is not found the software could restart the computation using a less strict discretization (requiring a lot more time).

## Slide 9: Examples

## Slide 10: 1 Region 1 Lab
Even with the problem generated with only for placing 1 region that needs 1 LAB block we can see the difference between the discretizing and completely free approach:
With Discretization: Time to optimize=0.5 sec
Complete Freedom: Time to optimize=163 sec

## Slide 11: More Regions
The next examples are generated using N regions with a requirement of 100 LAB and definitively discard the complete freedom approach.

## Slide 12: More Regions Results
 | Only Feasibility |  | With Objective Function | 
N.Of Regions | Discretized Version | Complete Version | Discretized Version | Complete Version
1 | 0.814 | >10 min | 0.809 | >10 min
2 | 1.477 | >20 min | 1.622 | >20 min
3 | 2.138 | >20 min | 2.162 | >20 min
4 | 2.861 | >20 min | 2.943 | >20 min
5 | 3.433 | >20 min | 3.508 | >20 min